## Slide 1: Photovoltaic Power Technology
Principles, Applications, and Future Trends

## Slide 2: What is Photovoltaic Technology?
• One of only two methods to generate significant electric power
• Discovered by Becquerel in 1839, developed as power source in 1954
• Converts sunlight directly into electricity with no moving parts
• Based on semiconductor physics and the photovoltaic effect

## Slide 3: How Photovoltaic Cells Work
1. Photons from sunlight strike semiconductor material
2. Photons with sufficient energy create electron-hole pairs
3. Built-in electric field at p-n junction separates charges
4. Electrons flow through external circuit as electric current
5. Typical silicon cells produce ~0.5-0.6V

## Slide 4: The P-N Junction: Heart of a Solar Cell
• P-type: Silicon doped with boron (has 'holes' or positive carriers)
• N-type: Silicon doped with phosphorus (has excess electrons)
• Junction creates built-in electric field and depletion region
• Light creates electron-hole pairs that are separated by this field
• This charge separation generates voltage and current

## Slide 5: Electrical Characteristics
• Short-circuit current (Isc): Maximum current when V=0
• Open-circuit voltage (Voc): Maximum voltage when I=0
• Fill factor: Ratio of maximum power to product of Isc and Voc
• Maximum power point: Optimal operating point on I-V curve
• Temperature effects: Power decreases as temperature increases

## Slide 6: Efficiency Limitations
• Photons with energy less than band gap (~23% loss)
• Excess photon energy lost as heat (~33% loss)
• Voltage factor losses (~20% loss)
• Fill factor and collection inefficiencies (~22% combined)
• Theoretical limit (Shockley-Queisser): ~31% for single-junction

## Slide 7: PV Cell Technologies
First Generation: Crystalline Silicon (80% of market)
  • Single-crystal Si (15-25% efficiency)
  • Multi-crystalline Si (13-20% efficiency)
Second Generation: Thin Film Technologies
  • Amorphous Si, CdTe, CIGS (7-20% efficiency)
Third Generation: Multi-junction cells, concentrators
  • Up to 44% efficiency with concentration

## Slide 8: PV System Applications
Grid-Connected Systems (97% of global installations)
  • Rooftop installations (residential/commercial)
  • Building-integrated PV (BIPV)
  • Utility-scale solar farms
Stand-Alone Systems
  • Rural electrification in developing countries
  • Telecommunications, water pumping, lighting

## Slide 9: Market Growth & Economics
• Explosive growth: 200 MW in 1990 → 80+ GW in 2012
• Cost reduction: $40/W in 1980s → ~$1/W in 2013
• Grid parity achieved in many regions
• Positive feedback loop: Policy → Demand → Production → Lower costs
• Energy payback time: 2-3 years (temperate climate)

## Slide 10: Environmental & Social Benefits
• Zero emissions during operation
• No noise pollution
• Long lifetime (20+ years guaranteed, much longer expected)
• Rural electrification in developing nations
• Energy independence and security

## Slide 11: Future Outlook
• Continued efficiency improvements
• Further cost reductions through manufacturing scale
• Building integration becoming standard
• New materials and concepts (perovskites, organic PV)
• PV becoming mainstream electricity generation worldwide

## Slide 12: Conclusion: PV Power Advantage
• Universal applicability (solar radiation available everywhere)
• Modular nature (scalable from watts to megawatts)
• Reliability, long life, ease of use
• No emissions, no noise, minimal maintenance
• Continuing improvements in technology and cost

## Slide 13: Questions?